| Serial Number | Name of Parameter | Benchmark | Averaged over a period |
| --- | --- | --- | --- |
| (i) | Fault incidences (No. of faults/100 subscribers /month) | ≤ 5 | One Quarter |
| (ii) | Fault repair by next working day | For urban areas: By next working day: ≥ 90% and within 3 days: 100%. For rural and hilly areas: By next working day: ≥ 90% and within 5 days: 100%. Rent Rebate Faults pending for >3 days and ≤7 days: Rent rebate for 7 days. Faults pending for >7 days and ≤15 days: Rent rebate for 15 days. Faults pending for >15 days: rent rebate for one month. | One Quarter |
| (iii) | Mean Time To Repair (MTTR) | ≤ 8 Hrs | One Quarter |
| (iv) | (a) Call Completion Rate within a local network shall be better than | ≥ 55% | One Quarter |
|  | or, |
|  | (b) Answer to Seizure Ratio (ASR) | ≥ 75 % | One Quarter |
| (v) | Point of Interconnection (POI) Congestion (on individual POI) | ≤ 0.5% | One month |
| (vi) | Metering and billing credibility – post paid | Not more than 0.1% of bills issued should be disputed over a billing cycle | One Billing Cycle |
| (vii) | Metering and billing credibility –- pre-paid | Not more than 1 complaint per 1000 customers, i.e., 0.1% complaints for metering, | One Quarter |

| Serial Number | Name of Parameter | Benchmark | Averaged over a period |
| --- | --- | --- | --- |
| (i) | Provision of a telephone after registration of | 100% in ≤ 7 days (subject to technical feasibility) | One quarter |
| registration of demand |
| (ii) | Shift of Telephone Connection | ≤ 3 days (95% of requests to be attended within 3 days) | One quarter |
| (iii) | Grade of Service | (a) Junctions between local exchanges – 0.002 (b) Outgoing junctions from Trunk Automatic Exchange (TAX) to local exchange – 0.005 (c) Incoming junctions from local exchange to TAX – 0.005 (d) Incoming or out going junctions between TAX’s 0.005 (e) Switching network should be non-blocking or should have extremely low blocking probability. |

Quality of Service parameters to be reflected in customer perception of service…..

| Serial Number | Name of Parameter | Benchmark |  |
| --- | --- | --- | --- |
| (a) | customers satisfied with the provision of service | ≥ 90 % |  |
| (b) | customers satisfied with the billing performance | ≥ 95 % |  |
| (c) | customers satisfied with network performance, reliability and availability | ≥ 95 % |  |
| (d) | customers satisfied with maintainability | ≥ 95 % |  |
| (e) | customers satisfied with supplementary and value added services | ≥ 90 % |  |
| (f) | customers satisfied with help services including customer grievance redressal | ≥ 90 % |  |
| (g) | customers satisfied with overall service quality | ≥ 90 % |  |

Quality of Service parameters in respect of which compliance reports are to be submitted to the Authority for cellular:

| Serial Number | Name of Parameter | Benchmark | Averaged over a period |
| --- | --- | --- | --- |
| A | Network Service Quality Parameters: |
| (i) | Network Availability |
| (a) BTSs Accumulated downtime (not available for service) | ≤ 2% | One Month |
| (b) Worst affected BTSs due to downtime | ≤ 2% | One Month |
| (ii) | Connection Establishment (Accessibility) |
| (a) Call Set-up Success Rate (within licensee's own network) | ≥ 95% | One Month |
| (b) SDCCH/ Paging Channel Congestion | ≤ 1% | One Month |
| (c) TCH Congestion | ≤ 2% | One Month |
| (iii) | Connection Maintenance (Retainability) |
| (a) Call Drop Rate | ≤ 2% | One Month |
| (b) Worst affected cells having more than 3% TCH drop (call drop) rate | ≤ 5% upto 31.03.2011 ≤ 3% From 01.04.2011 | One Month |
| (c) connections with good voice quality | ≥ 95% | One Month |
| (iv) | Point of Interconnection (POI) Congestion ( on individual POI) | ≤ 0.5% | One Month |
| B | Customer Service Quality Parameters: |
| (v) | Metering and billing credibility – post paid | Not more than 0.1% of bills issued should be disputed over a billing cycle | One Billing Cycle |
| (vi) | Metering and billing credibility –- pre-paid | Not more than 1 complaint per 1000 customers i.e. 0.1% complaints for metering, charging, credit, and validity | One Quarter |
| Serial Number | Name of Parameter | Benchmark |
| 1 | Service Coverage | For In-door coverage the signal strength at street level shall be ≥ -75 dBm and In-vehicle shall be ≥ -85 dBm. |